Manual delete of mYsql service

## error message

N/A

## Applies to

- IMSMA NG 5.06.02 to 5.08.04

## Exceptions

No exceptions are known.

## Reason

Something went wrong during installation or the MySQL service is needed to be deleted.

## Solution

How to verify that the MySQL service is stopped may be done in different ways

1	Right-click on My Computer in the Start menu, in the File Explorer or on the Desktop. Choose Manage in the menu.

OR

1	Got to Control Panel, Administrative tools and Services.

2	In Services find MySQL and verify that the Status not is Started. If the status is Started then right-click on the row and choose Properties.

3 	Click on Stop and then on OK.

4	Start the DOS prompt by e.g. choosing Run, type cmd and click on OK.

5 	Type cd c:\imsmang\mysql\bin and press Enter

6	Type mysqld --remove MySql

Press Enter

7	If you did not received any error message, type Exit to close the DOS prompt and press Enter.

8	DO NOT TRY TO INSTALL THE SERVICE BEFORE RESTARTING THE COMPUTER.

9	Restart the computer

10	If you want to install the service there is another Technical note describing how to

do that.